## Slide 1: Underground Utility Damage Investigation
Reliability Field Guide Aligned with CGA DIRT Reporting
Structured method for evaluating damages and identifying preventable causes

## Slide 2: Purpose
Document events using recognized industry reporting elements
Identify the first preventable cause to reduce recurrence
Strengthen investigative discipline alongside CGA DIRT reporting

## Slide 3: Investigation Flow
DEFINE → MEASURE → ANALYZE → CLASSIFY → CORRECT
Follow this sequence on every damage
Premature conclusions weaken investigations

## Slide 4: Investigator Responsibilities
Secure the site before investigating
Preserve evidence before conditions change
Remain neutral and follow facts
Evaluate both excavation and locating systems
Recommend system-level corrections

## Slide 5: Immediate Actions Upon Arrival
Verify hazards are controlled
Confirm emergency response if required
Ensure the facility is stabilized
Begin investigation only after the scene is safe

## Slide 6: Preserve Perishable Evidence
Photograph utility markings, damage point, and excavation path
Capture equipment positioning, spoil piles, and depth indicators
Document surrounding utilities and work zone layout
Markings disappear quickly — capture them first

## Slide 7: DEFINE — Establish the Event
Create a factual description using verified information only
Record date, time, location, facility damaged, work underway, and stakeholders
Document immediate impacts such as outage, release, injury, or evacuation
Avoid opinions or blame language

## Slide 8: DIRT Core Data Elements
Facility operation affected and installation type
Damage type and confirmed impacts
Service interruption, product release, injury, or evacuation
Document facts only

## Slide 9: Excavator Information
Excavator type and company name
Was the excavator also the facility owner?
Crew onsite and experience level
Type of work being performed and equipment used

## Slide 10: Notification Review (811)
Was 811 notified and was the ticket valid?
Did the ticket match the work area?
Was white lining used where appropriate?
Were all utilities notified and did they respond?

## Slide 11: Locate Review
Who performed the locate?
Were markings present, visible, and complete?
What records supported the locate?
Was congestion evident or were mapping limitations known?

## Slide 12: Excavation Conditions
Method used and equipment type
Tolerance zone identified
Evidence of potholing or exposure
Alignment with markings and soil conditions

## Slide 13: Site Complexity Indicators
Utility congestion or recent installations
Abandoned facilities or inconsistent depths
Limited access or environmental interference
Higher complexity requires stronger safeguards

## Slide 14: ANALYZE — Visible Cause
State the physical action only
Examples: bucket contacted gas main, bore struck fiber
The visible cause is not the root cause

## Slide 15: Identify the First Preventable Cause
Use sequential 'Why' questions
Continue until reaching a controllable condition
Stop when the cause identifies something the organization could influence

## Slide 16: Root Cause Format
Visible Cause = Physical event
First Preventable Cause = Controllable breakdown
Avoid long narrative explanations

## Slide 17: CLASSIFY — Behavioral Driver
Determine whether the issue was Aptitude or Attitude
Match organizational response to the behavioral driver

## Slide 18: Aptitude (Capability Gap)
Use when knowledge, preparation, or skill was insufficient
Examples: misinterpreted markings or improper locating technique
Respond with training, mentorship, and procedural improvements

## Slide 19: Attitude (Commitment Gap)
Use when expectations were understood but disregarded
Examples: ignored markings or excavated without notification
Respond with accountability, contract enforcement, or oversight

## Slide 20: Dual-System Review
Evaluate both operational narratives
Investigate systems — not sides
Most damages involve layered contributors

## Slide 21: Excavation System
Did the work environment support safe digging?
Notification completed and tolerance zones respected?
Verification attempted when risk increased?
Were field decisions reasonable?

## Slide 22: Locating & Infrastructure System
Did the excavator receive a reasonable opportunity to succeed?
Records available and marks reliable?
Mapping current and uncertainty communicated?

## Slide 23: CORRECT — Reduce Recurrence
Define actions tied directly to the preventable cause
Examples: require verification near crossings
Strengthen mapping governance and revise training requirements
Avoid vague recommendations

## Slide 24: Leadership Validation
If this job were repeated tomorrow, would the outcome improve?
If uncertain, corrective actions are incomplete

## Slide 25: Evidence Checklist
Photographs, ticket records, and locate documentation
Witness statements and field notes
Supervisor input and as-built records
Base conclusions on documented evidence

## Slide 26: Investigator Principles
Remain objective
Separate conditions from behavior
Identify controllable causes
Convert every damage into operational learning

## Slide 27: Field Reminder
Visible Cause = What happened
Preventable Cause = What must change
Reliable investigations strengthen reliable systems

## Slide 28
Investigation Flow Diagram
DEFINE
MEASURE
ANALYZE
CLASSIFY
CORRECT

## Slide 29
Dual-System Investigation Model
Excavation System
Locating & Infrastructure System
Damage Event

## Slide 30
Root Cause Identification Path
Visible Cause
Why?
Why?
Why?
First Preventable Cause

## Slide 31
Aptitude vs Attitude Decision Tree
Was the expectation
clearly understood?
APTITUDE (Capability Gap)
• Training
• Mentorship
• Skills Validation
• Procedure Improvement
ATTITUDE (Commitment Gap)
• Accountability
• Contract Enforcement
• Oversight
• Corrective Action
NO
YES

## Slide 32
Swiss Cheese Model — Layered Safeguard Failure
Planning
811 Notification
Locating
Marking
Verification
Excavation Practices
Damage

## Slide 33
Human vs System Failure
Human Factors
• Decision Making
• Situational Awareness
• Skill Level
• Fatigue
System Factors
• Training Programs
• Mapping Quality
• Procedures
• Communication
Outcome

## Slide 34
Preventable vs Non‑Preventable Decision Tree
Could the organization
reasonably control
this condition?
PREVENTABLE
• Improve process
• Add safeguards
• Strengthen training
NON‑PREVENTABLE
• Document conditions
• Share lessons
• Monitor trends

## Slide 35
Excavation Risk Escalation Ladder
Low Risk
(Open area, clear marks)
Moderate Risk
(Close tolerance zone)
Elevated Risk
(Congestion / crossings)
High Risk
(Conflicting data)
Critical Risk
(Unknown facilities)
Increasing
Control

## Slide 36
Reliability Lifecycle Model
Plan
Locate
Verify
Excavate
Investigate
Improve